## Slide 1
Fire mapping w Shortwave Infrared
Ash Richardson, Predictive Services Unit
BC Gov RS CoP 2022 Apr 13, 11:30

## Slide 2: Overview
Pre-process
Fire Detection method #1
  And Perimeter recipe
Fire Detection method #2
  Deal w clouds/ice without Level2-processing cloud mask!
Appendix:
  Visualize results of Sen2Cor

## Slide 3: Satellite mapping of fires
Remote areas: less costly, safer compared to heli-GPS perimeters
Cost effective, timely BI for fires being monitored
Fire growth modelling & other predictive services require daily perimeter updates to reduce simulation error
Complement other methods: airborne-GPS and IR scanning (less frequent as fires get large/ smoke conditions limit visibility)
Provide additional info about recent fire activity along a perimeter, helping refine model inputs
Start with Sentinel-2.. Add more?

## Slide 4: SWIR for fire mapping?
"Unlike TIR imaging, smoke is not transparent at these wavelengths but SWIR has somewhat better haze and smoke penetration than visible light" [1]
Historically SWIR more popular for monitoring volcanoes than forest fires.. (DGG)
Increasing popularity of SWIR for forest fires
  Connected with / enhanced by Machine Learning algorithms [3]
[1] (2016) R.S Allison, J. M. Johnston, G Craig and S. Jennings, "Airborne Optical and Thermal Remote Sensing for Wildfire Detection and Monitoring
[2] (2004) Vis with fires = orange / red https://www.youtube.com/watch?v=lp1fj2Vx6fY
[3] (2021) Automated classification of heat sources detected using SWIR remote sensing
https://www.sciencedirect.com/science/article/pii/S0303243421001987

## Slide 5: Pre-processing steps
Sen2cor processing (L1C --> L2A)*
Retain
  B12 2190nm (20m), B11 1610nm (20m), B9 945nm (60m)
Resample to 20m
  (Why? bands of interest: 20m, 20m, 60m)
Sort bands in order: wavelength increasing**
*Still need this for now. Also might want to bring the B10 back!
** Always sort data if:
We can
It makes physical sense to do so
Why?
Easier to follow the story
Sorting is the only thing computers can do (proof by "SUBLEQ" OISC)

## Slide 6: Processing steps
Individual bands (increasing)

## Slide 7: Satellite-based fire perimeter recipe
Threshold (create a fire mask)
Flood (identify pieces of fire)
Link (put pieces together)
Trace (a linear boundary)
  Exclude segments less than certain size
  Alpha hull --> geolocate the coords
  Create KML

## Slide 8: Small fire example RGB = RGB (visible) RGB= (B12, B11, B9) shortwave IR

## Slide 9: 1. Threshold
[please click here for source code]

## Slide 10: 2. Flood fill
[please click here for source code]

## Slide 11: 3. Link
[please click here for source code]

## Slide 12: 4. Trace
[please click here for source code]

## Slide 13: Big fire example RGB = RGB (visible) RGB= (B12, B11, B9) shortwave IR

## Slide 14: 1. Threshold

## Slide 15: 2. Flood fill

## Slide 16: 3. Link

## Slide 17: 4. Trace
Manually select cluster
Or scrub unwanted areas

## Slide 18: Beware the L7
Sacrelige

## Slide 19: Beware the L8

## Slide 20: Prisma (ASI). SpecInterp to S2, apply Method #1 and compare w S2:

## Slide 21: White Rock Lake Fire L7/8 included

## Slide 22: Method 2: dominant band

## Slide 23: Method 2: dominant band

## Slide 24: "Better method"
False positive: urban target

## Slide 25: Can we use L2 class map?
From Sen2Cor (ESA)
Results don't look great!
Check snow class (value 11)
Smoke gets marked as snow
Need ML for more reliable/ Contextual land cover
ML can respond to new training and compensate for lack of calibration

## Slide 26: Method 2: dominant band

## Slide 27: Method 2: dominant band
Dana!

## Slide 28: Next steps?
Accessible stepping stone towards actual Machine Learning
Work w Devona & team to meet BCWS standards
Work w Ben & Neal to support fire simulations
Automate addition of Landsat 7/8/9
Remove nonveg/urban/water
Recency of detection
Work w Agile team
More satellites
Possibilities:
Combine immediate info with before/after info
First-principles physics modelling to derive spectra

## Slide 29: L1 Sentinel-2.. Sen2Cor not applied GML (аеропорт Гостомель)

## Slide 30: L2 Sentinel-2.. Sen2Cor applied GML (аеропорт Гостомель)

## Slide 31: Possibilities
ENVI samples = 10980 lines = 10980 bands = 4 header offset = 0 file type = ENVI Standard data type = 4 interleave = bsq byte order = 0 band names = {20220226 60m: B9 945nm, 20220226 60m: B10 1375nm, 20220226 20m: B11 1610nm, 20220226 20m: B12 2190nm}
"swir.hdr" 13L, 251C Then raster_sub_compare.cpp
1) Subselect SWIR from L1 (4 bands)
2) perform combinatorial differencing